## Slide 1: Advanced SDR Ham radios vhf, UHF, Microwaves
John Petrich, W7FU
MUD 2017
October 27, 2017

## Slide 2: GOAL
Inspire you to approach microwave station building in a different way

## Slide 3: Presentation Outline
Review advanced SDR Microwave hardware and ‘ham friendly’ DSP software
Ham Microwave rigs: examples and ideas
Note: heavy emphasis on homebrewing

## Slide 4: What’s ‘Advanced’ about modern SDR’s?
SDR digital hardware integrated with RFIC transceivers, to provide direct conversion for VHF/Microwave frequencies
- developed for cell phone industry
- optimized for VHF/lower Microwave use
  - low noise, high S/N ratio, RF linearity, frequency stability, and dynamic range
‘Ham Friendly’ DSP software tools readily available to hobbyists

## Slide 5: SDR: The New Normal?
Wide design flexibility in terms of modulation bandwidth and frequency coverage
High performance signal processing
Simplified system design using a wideband
direct conversion SDR

## Slide 6: Advanced SDR Hardware
Development lab, test and measurement, education oriented, and not cheap
Easily repurposed to ham use
Assumes considerable self-learning based on first principles

## Slide 7: Advanced SDR Hardware Choices
Ettus Research USRP
www.Ettus.com/products
Nuand/Blade RF
www.Nuand.com
Hack RF
http://www.greatscottgadgets.com/
Lime SDR
www.limemicro.com/products/software-defined-radio/

## Slide 8: Advanced SDR Hardware
Hardware Example
Ettus Research USRP, B200/210 SDR transceiver
direct conversion from 50 MHz to 6 GHz
  state of the art RF & baseband performance
  low phase noise frequency synthesizers
  optional external master clock
  TX RF output >> +5 dBm
  RX ~2+ dB NF
  single board solution (6” x 4”) or (3.25” x 2”)

## Slide 9: Advanced SDR Hardware

## Slide 10: Advanced SDR Hardware
Ettus USRP B210 SDR Transceiver

## Slide 11: Advanced SDR Hardware
Ettus USRP B200 SDR Transceiver

## Slide 12: Native Performance Examples
Transmitter Spurious Output, Phase Noise, and Linearity

## Slide 13: Microwave Spectral Purity
Wideband Transmit Spectrum @ 2.3 GHz

## Slide 14: VHF Harmonic Analysis
Harmonic Analysis @ 144 MHz (typical)

## Slide 15: Microwave Phase Noise
Phase Noise: 5.8 GHz @10 kHz RBW

## Slide 16: Microwave Transmit Linearity
Two Tone LSB: 5.8 GHz @10 kHz RBW

## Slide 17: ‘Advanced’ DSP Software
GNU Radio: “Ham Friendly DSP”
Open source DSP library: supported in Linux, Windows, OSX, operating systems
Graphical DSP authoring simplified
Optimized for ‘real time’ signal processing
(VOLK, C++ API)
Supports transmit and receive DSP

## Slide 18: GNU Radio DSP Flow Graph
SSB Phasing Transmitter DSP

## Slide 19: GNU Radio DSP GUI

## Slide 20: Receiver Bandwidth Spectrum
Receiver Bandwidth 3 kHz

## Slide 21: Advanced’ DSP Software
SoDa Radio: Custom Ham Software
Matt Reilly, KB1VC
Custom ham oriented DSP software
Open source, free download
Linux OS
All mode, Transmit and Receive DSP
Written for the full Ettus USRP product line: UHD

## Slide 22: ‘Advanced’ DSP Software
GNU Radio
GNU Radio home page: https://wiki.gnuradio.org/
Ham Friendly DSP:
https://w7fu.com/
SoDa Radio
https://kb1vc.github.io/SoDaRadio/

## Slide 23: SDR Examples: What you can do with this stuff
Test and Measurement
Signal Source: synthesized frequency
RF and IF Spectrum Analyzer: ~ 25 MHz instantaneous bandwidth, high sensitivity
Scaler Network Analyzer: point by point

## Slide 24: SDR Examples: What you can do with this stuff
Microwave Radios
Direct Conversion radio architecture:
VHF and lower Microwave bands

## Slide 25: Traditional Conversion to Microwaves
High performance HF transceiver
Outboard Linear Up-converter(s) per band
Custom per band RF ‘interface’
Linear
Up-converter
HF
Transceiver Transceiver
Power Amplifier LNA Tx/Rx relay

## Slide 26: Direct Conversion SDR Ham Microwave Radio System
High performance direct conversion SDR broadband transceiver
Custom per band RF PA and LNA
Microwave SDR Transceiver
Power Amplifier
LNA Tx / Rx relay
Signal

## Slide 27: Direct Conversion SDR: VHF/UHF/Microwave
VHF/UHF/uW Antenna
FPGA
DSP
signal
RFIC
(mixer)
A/D Converter
(baseband)
Computer
DSP
data
D/A
Converter
data
signal
analog
data
baseband
Etc..

## Slide 28: Direct Conversion SDR: VHF/UHF/Microwave

## Slide 29: 5.7 GHz SDR - Rover Station

## Slide 30: SDR Examples: What you can do with this stuff
Microwave Radios
Double Conversion radio architecture: upper Microwave and mm Wave bands
Flexible IF choices: 50 MHz to 6 GHz
Any modulation including JT modes

## Slide 31: Double Conversion SDR Traditional Architecture: VHF IF
Microwave Antenna
signal
DBM
(mixer)
A/D Converter
(baseband)
Computer
DSP
data
D/A
Converter
data
signal
analog
data
baseband
Etc..
VHF IF frequency with SDR direct conversion to
baseband

## Slide 32: 24 GHz Transverter: 144 MHz SDR IF

## Slide 33: Double Conversion SDR: Novel Approaches
Microwave Antenna
signal
DBM
(mixer)
A/D Converter
(baseband)
data
D/A
Converter
data
Mixed signal
Etc..
DSP
SDR TX #2
for LO signal
LO input
LO
IF
RFIC
(mixer)

## Slide 34: 10 GHz Transverter v.1: Integrated SDR IF and LO
Dual Transceiver SDR: Ettus B210 SDR
IF: ~1.3+ GHz with direct conversion to baseband
LO: ~1.3 GHz (X7) using SDR transmitter #2 for the10 GHz mixer LO signal (from RFIC frequency synthesizer and FPGA numerically controlled oscillator (NCO))

## Slide 35: 10 GHz SDR Transverter v.1

## Slide 36: 10 GHz Transverter Tune-up

## Slide 37: 10 GHz Transverter v.2: Integrated SDR IF and LO
Dual Transceiver SDR: Ettus B210
plus
Mini-Circuits SIM-153+ mixer
IF: 5.1881 GHz
LO: 5.1800 GHz
RF: 10.3681 GHz

## Slide 38: 10 GHz SDR Transverter v.2

## Slide 39: In Conclusion
I hope that you are stimulated by the possibilities
Thanks to Ray, W7GLF for his support on getting this equipment on the air
Thanks to the MUD 2017 organizers for the opportunity to present this material

## Slide 40: Down the Slippery Slope…
More information about DSP and SDR
www.w7fu.com

## Slide 41: Additional Questions ?
Hardware ?
Software ?
Other related topics ?