## Slide 1: Ham Friendly Digital Signal Processing
John Petrich, W7FU
mailto:petrich@u.washington.edu
ARRL NW Division Convention
Seaside, OR
June 2016

## Slide 2: Agenda
Discuss relationship of DSP and SDRs
Introduce GNU Radio: open source, graphical programming
Demonstrate a selection of DSP operations: FM radio, Panadapter,
filter, wave form generator, audio output
How to get started with GNU Radio – resources, nuts and bolts

## Slide 3: SDR and DSP Fundamentals
All radio receivers process signals and output to ‘baseband’:
  IF, filters, detectors, audio output
SDR receiver digitizes radio signals to baseband:
  direct conversion and direct sampling
DSP software processes the baseband data to complete the radio
The software is the DSP, the DSP is the software, DSP is the radio

## Slide 4: Key Takeaways
DSP uses same signal flows as traditional analog radio
DSP uses same processes – mixers, filters, amplifiers, etc.
DSP is much simplified in comparison- no concern about
impedance matching, signal leakage, and filtering
DSP offers higher performance due to unmatched digital precision

## Slide 5: SDR Terminology
Direct Conversion: converts RF to digital baseband with no IF stage
Direct Sampling: A/D and D/A converters have huge baseband and can operate at RF. No need for direct conversion
FPGA: a logic block for initial DSP located on the SDR hardware
Data Interface: can be USB 2.0, 3.0, or Ethernet to computer

## Slide 6: Realities of Homebrew SDR
Modern SDR hardware miniaturized - components require automated assembly
SDR hardware can be paired with multiple different software applications: e.g. SDR#, HRD, SDR Console, and others
DSP software is where the ham can homebrew SDRs. GNU Radio is the soldering iron equivalent for modern SDR building projects. DSP is the radio.

## Slide 7: GNU Radio
Open source: no cost, ‘rolling’ development always an adventure
Linux Ubuntu OS preferred, Windows and Mac OS also possible
GNU Radio optimized for ‘real time’ signal processing as different from simulation or modeling see and hear signals “now”
Graphical programing – connect DSP ‘blocks’: ideal for hams more interested in their radio than their computers

## Slide 8: GNU Radio Demonstration
1) FM Radio using inexpensive RTL SDR
2) Panadapter display
3) Digital Filter with variable bandwidth
4) Waveform generator
5) Audio output

## Slide 9: How to Get Connected with GNU Radio
Primary Information Sources
GNU Radio primary portal: http://www.gnuradio.com
GNU Radio Ham Radio Wiki URL: http://www.http://gnuradio.org/redmine/projects/gnuradio/wiki/HamRadio
GNU Radio for Beginners: http://www.w7fu.com everything you need to know to get started.

## Slide 10: How to Get Started with GNU Radio
GRC ‘get started’ Wiki with instructions: http://www.http://gnuradio.org/redmine/projects/gnuradio/wiki/InstallingGR
Live GNU Radio: Simple “boot and go”. Bootable USB memory stick or CD with Linux Ubuntu and GNU Radio pre-installed. Make it yourself or purchase. No changes to your hard drive or native OS.
Dual boot installation of Linux Ubuntu and GNU Radio. Best method for serious work. “Virtual’ machines only for simulation.

## Slide 11: In Conclusion
I want to thank
Howard Burns, W1HMB
and
Tom McDermott, N5EG
for their assistance with this presentation
Thanks also to SeaPac for the opportunity
to present this project at the 2016 ARRL NW Division Convention

## Slide 12: FAQ’s
Q: Does GNU Radio function with a Windows and Apple OS?
A: New installation scripts make installation more easy and less
problematic than in the past
Q: What type of computer is required?
A: Two cores @ 2500 MHz: i3 is minimum, I5 or i7 recommended
by the developers

## Slide 13: FAQ’s (continued)
Q: If I have questions or get lost, can I reach you?
A: Absolutely, I’ll do what I can to help.
mailto:petrich@u.washington.edu

## Slide 14: Additional Questions ?
Hardware ?
Software ?
Other related topics ?