## Slide 1: VHF - UHF - Microwave SDR Transceiver on the air
John Petrich, W7FU
ARRL NW Division Convention
SEA-PAC 2017
June 3, 2017

## Slide 2: Presentation Goals
Discover what is “under the hood” of a VHF SDR (or any SDR)
Learn “how to” build a practical VHF SDR - with photos
Address the question: “Do SDR’s have a place in VHF communications?”

## Slide 3: VHF - UHF SDR Home Station

## Slide 4: Microwave SDR Rover Station

## Slide 5: Dirty Little Secret
“These same principles apply to any
SDR station HF to Microwave”
All SDRs need an RF interface to the amplifiers and antenna
All SDRs need peripheral devices to control the radio and station

## Slide 6: Direct Sampling HF SDR
HF Antenna
A/D Converter
(Baseband)
FPGA DSP
signal
data
Computer DSP
Panadapter
D/A Converter
Audio
Analog
Data
data
data
Baseband

## Slide 7: Direct Conversion VHF SDR
VHF Antenna
FPGA
DSP
signal
Mixer RFIC
A/D Converter
(Baseband)
Computer
DSP
data
D/A
Converter
data
signal
Analog
Data
Baseband
Etc..

## Slide 8: What’s under the hood?
VHF / Microwave any-mode
SDR Transceiver
Direct conversion between RF and digital baseband
Single board solution with open source
DSP software

## Slide 9: SDR Description
Hardware
Ettus Research B210 SDR dual transceiver
  single board solution (6” x 4”) or (3.25” x 2”)
  State of the art RF & baseband performance
  TX RF output > +5 dBm, RX ~2+ dB NF
  Software DSP
GNU Radio open source software DSP library
  Linux, Windows OS platform
  Graphical DSP authoring

## Slide 10: Advanced SDR Hardware
Ettus USRP B210 SDR Dual Transceiver

## Slide 11: ‘Advanced’ DSP Software
GNU Radio
Open source DSP library: (Linux, Windows, OSX, OS)
Graphical DSP authoring simplified
Optimized for ‘real time’ signal processing
(VOLK, C++ API)
Supports transmit and receive DSP

## Slide 12: GNU Radio DSP Flow Graph
SSB Phasing Transmitter DSP

## Slide 13: GNU Radio DSP GUI

## Slide 14: Performance Measures
Transmitter Spurious Output
and Harmonics

## Slide 15: Microwave Spectral Purity
Wideband Transmit Spectrum @ 2.3 GHz

## Slide 16: VHF Harmonic Analysis
Harmonic Analysis @ 144 MHz (typical)

## Slide 17: “How to”: VHF – UHF - Microwave SDR
What parts are involved?
How it is done?
What does a VHF to microwave SDR actually look like?

## Slide 18: SDR Transceiver

## Slide 19: SDR RF Interface

## Slide 20: SDR Peripherals

## Slide 21: Band Specific Power Amplifiers

## Slide 22: Band Specific Power Amplifiers

## Slide 23: VHF/Microwave SDR Station
Conceptual model in four parts:
Broadband, direct conversion,Transceiver
2) Broadband RF Interface
3) Band specific Power Amplifiers, antennas
4) SDR Peripherals: transceiver system
control

## Slide 24: SDR RF ‘Interface’
The RF Interface links the SDR with the rest of the RF system – antennas, amplifiers
Receiver input protection relay with termination, RFI filter for FM Broadcast
Low level transmit amplifier, T/R relay

## Slide 25: SDR ‘Peripherals’
The SDR Peripherals link all the SDR transceiver and rig control functions:
OCXO
Keying circuits
Memory keyer
PTT and amplifier control
T/R relay– sequencer
DC power distribution system

## Slide 26: All put together: Microwave SDR Rover Station

## Slide 27: Bend, OR - Rover QSO

## Slide 28: SDR: The New Normal?
Near ideal signal processing ability: ‘digital determinism’ – high performance
Supports all available amateur radio modulations and all VHF/UHF/lower Microwave frequencies -- - wide design flexibility
Integrates well with existing RF systems – simplifies system design
Size and weight attractive compared to
analog counterparts

## Slide 29: Typical Analog Ham VHF System
High performance HF transceiver
Outboard Linear Up-converter(s) per band
Custom per band RF ‘interface’
Linear
Up-converter
HF
Transceiver Transceiver
Power Amplifier LNA Tx/Rx relay

## Slide 30: Advanced SDR Ham VHF Radio System
High performance direct conversion SDR broadband transceiver
Custom per band RF ‘interface’
VHF/UHF SDR Transceiver
Power Amplifier
LNA Tx / Rx relay

## Slide 31: In Conclusion
I want to thank Barry Hansen, K7BWH,
Phil Horkin, AG7GY, Mariana Varotto, WA7EE
For their generous assistance with this project
Thanks also to the ARRL for the opportunity to present this project

## Slide 32: Down the Slippery Slope…
More information about DSP and SDR
www.w7fu.com

## Slide 33: Additional Questions ?
Hardware ?
Software ?
Other related topics ?