## Slide 1: Using GRC to Build Radios
Kick Start: help the novice to use the flow graph in GNU Radio
John Petrich, W7FU
www.w7fu.com/presentations

## Slide 2: Major Topics
Getting started with GRC
Basic flow graph workspace organization
Flow graph details
Data flow problem solving
Practical odds and ends for real radios
Group discussion

## Slide 3: Getting Started with GNU Radio
How to install GNU Radio
https://wiki.gnuradio.org/index.php/InstallingGR
Guided Tutorials
https://www.youtube.com/watch?v=N9SLAnGlGQs&list=PL618122BD66C8B3C4
(novice flowgraph techniques, an oldie but goodie)
https://wiki.gnuradio.org/index.php/Tutorials
(sophisticated and advanced techniques)

## Slide 4: Workspace Organization Why Important?
Promotes an understanding of signal processing logic
Makes flow graph modifications easier
Facilitates trouble shooting and problem solving
Reduces risk of workspace mistakes

## Slide 5: Workspace Organization

## Slide 6: Flow Graph Details
Options or ‘top block’
Note blocks
Block rotation
Virtual Sources and Sinks
Samp_rate logic and gain distribution
Nested Python commands to control multiple functions

## Slide 7: Options Block or ‘top block’

## Slide 8: Note Blocks
Keep track of your thinking

## Slide 9: Block Rotation

## Slide 10: Notes and Virtual Sources and Sinks

## Slide 11: Samp_rate Logic and Gain Distribution

## Slide 12: Nested Python Commands Control Multiple Parameters

## Slide 13: Nested Python Commands Control Multiple Parameters

## Slide 14: Nested Python Commands Control Multiple Parameters

## Slide 15: Flow Graph Problem Solving
Source and Sink not in your DSP library
Console data interpretation
Version and subversion problems
Signal tracing
Fractional resampler - ‘U’ and ‘aU’ interruptions
Bypass block option
Undo button on task bar

## Slide 16: Source and Sink Drivers not in DSP Library
Solution: Download and install driver for your hardware
Pluto SDR
Https://wiki.gnuradio.org/index.php/PlutoSDR_Source
Lime SDR
https://medium.com/bugbountywriteup/limesdr-setup-with-gnuradio-gr-limesdr-and-gqrx-on-ubuntu-20-04-4b275176d7cd
HackRF
https://github.com/mossmann/hackrf/wiki/Getting-Started-with-HackRF-and-GNU-Radio

## Slide 17: Console Data – GRC version + samp_rate error

## Slide 18: Console Data – error corrected

## Slide 19: Version Problems: GRC v3.7 vs. v3.8
Version 3.7 flow graphs will not run on a Version 3.8 installation:
a blank workspace
Version 3.8 flow graphs will not run on a Version 3.7 installation:
missing blocks
Solution: Hand build flow graph: block by block, parameter by parameter from your DSP library. Not a Copy and Paste solution

## Slide 20: GRC v3.7 Subversion Problems: missing blocks
Solution: Replace missing blocks with blocks from your DSP library

## Slide 21: GRC v3.7 Subversion Problems: global failure
Solution: Try replacing Source and Sink blocks first. Otherwise, hand
Rebuild from your DSP library.

## Slide 22: Signal Tracing and Stimulus Response Testing
Signal Tracing: Output to an instrumentation GUI widget, e.g.
FFT display to study data stream frequency components
Stimulus Response testing: Use a Signal Source or Noise Source
to study frequency response of filters, phase shifters, etc.

## Slide 23: Fractional Resampler ‘U’ and ‘aU’ Interruptions
Adjust ‘Ratio’ GUI slider to reduce ‘U’ and ‘aU’ interruptions

## Slide 24: Block ‘Bypass’ Option
A convenient means to functionally remove a block from a data stream.
<Right> click block and select <Bypass> from menu
Unbypassed block Bypassed block

## Slide 25: ‘Undo’ Button on Task Bar
Easy way to undo workspace mistakes, especially common with congested flow graphs using computers with touch pads, small screens

## Slide 26: Odds and Ends
Eliminate Receiver DC artifact
Selector switch
Analog TX/RX hardware logic control schematic
Software TX/RX control using duplex mode

## Slide 27: Eliminate Receiver DC Artifact
Solution: Offset Source center frequency and Freq Xlating filter center frequencies by the same amount in opposite directions, e.g. +/- 100e3 Hz

## Slide 28: Eliminate Receiver DC Artifact Properties Boxes

## Slide 29: Selector Switch
Selector interrupts data flow and turns off Sink. Useful for hardware derived logic for TX/RX switching systems.

## Slide 30: Analog TX/RX Hardware Control
Solution: Use a small amount of current from the SDR RX or TX LED
as a logic source. Use the current to drive a high gain transistor switch
array. The transistor switch then controls other system switches and
relays, i.e. PA’s, preamplifiers, antenna relays, etc.

## Slide 31: Analog TX/RX Hardware Control Schematic Diagram

## Slide 32: Software TX/RX Control: Duplex Mode
Solution: Use nested commands
Receive mode: The Source center frequency is selected for the desired operating frequency. The Sink center frequency is selected to “0” frequency. (or some out-of-bounds frequency)
Transmit mode: The Sink center frequency is selected for the desired operating frequency. The Source center frequency is selected to “0” frequency. (or some out-of-bounds frequency)

## Slide 33: Software TX/RX Control: Duplex Mode

## Slide 34: Group Discussion
What additional flow graph techniques do you want to share?
What are your current GRC projects or problems?